## Slide 1
PINN-Aided Gravity Anomaly
Map Matching for GNSS-Denied
Inertial Navigation
AME 508 · Machine Learning and Computational Physics · Spring 2026
Hojung Lim · Souvik Chatterjee · Kenneth Tseng
May 2026

## Slide 2
Motivation & Objective
⚡ The Problem
GPS jamming, underwater missions, and space operations make GNSS unavailable — yet precise navigation is still required.
📉 The Gap
IMU-only dead reckoning accumulates unbounded drift due to sensor bias and noise, quickly rendering position estimates useless.
🌍 Why Gravity?
Earth's gravity field varies spatially. Matching onboard gravimeter readings to a pre-learned PINN map provides position-fixing without any external signal.
01
Learn δg
Train a PINN on GGMplus data to predict residual gravity anomaly δg from position (lat, lon, alt).
02
Generate Innovation
Compare PINN prediction to onboard gravimeter reading to form an EKF innovation term ν.
03
Correct INS Drift
Use the EKF — with Jacobian H computed via autograd — to suppress IMU dead-reckoning error without GNSS.

## Slide 3
Algorithm & Architecture
EKF EQUATIONS
Predict Step
x̂ₖ|ₖ₋₁ = F x̂ₖ₋₁|ₖ₋₁
Pₖ|ₖ₋₁ = F Pₖ₋₁|ₖ₋₁ Fᵀ + Q
Update Step
νₖ = δg_meas − δg_PINN(x̂ₖ|ₖ₋₁)
Kₖ = Pₖ|ₖ₋₁ Hᵀ (H Pₖ|ₖ₋₁ Hᵀ + R)⁻¹
x̂ₖ|ₖ = x̂ₖ|ₖ₋₁ + Kₖ νₖ
Pₖ|ₖ = (I − Kₖ H) Pₖ|ₖ₋₁
H = ∇ₓ δg_PINN (via autograd — no manual derivation)
PINN ARCHITECTURE
Input
(lat, lon, alt)
4× Dense 64
Tanh + Skip connections
Output
δg (mGal)
16,961
Params
4 layers
× 64 neurons
Tanh
Activation
Skip
Connections

## Slide 4
Loss Function & Training
LOSS FUNCTION
L_total = L_data + λ · L_physics
L_data (Absolute + Relative Error)
Combines absolute error and relative error to prevent low-altitude bias — surface gravity is much larger than at altitude, so absolute error alone would overweight the ground level.
L_physics (Laplacian Constraint)
Enforces ∇²(δg) = 0 at collocation points — the Laplace equation for gravity in free space. Prevents overfitting and ensures physical consistency.
Boundary Condition
δg(r) = ω_NN(r)·δg_NN(r) + ω_BC(r)·δg_BC(r)
Weighted blend — no separate BC loss term needed.
TRAINING
32,768
Training Samples
(64×64 grid × 8 alt levels)
0.20%
Test Relative Error
vs. 0.30% paper benchmark
2,000
Training Epochs
Adam lr=2⁻⁸, λ=10⁻³
Data Source
GGMplus N30W120 tile (USC Campus, 34.02°N 118.29°W)
Sampling
64×64 uniform grid × 8 altitude levels (0–200 m)
Normalizer
StandardScaler fitted to local USC subgrid (Test 1)
or full tile range (Test 2) — this difference is key
Split
70% train (22,937) / 15% val (4,915) / 15% test (4,916)
Optimizer
Adam · lr = 2⁻⁸ · batch = 512 · λ = 10⁻³
Benchmark
Outperforms PINN-GM-III (Martin & Schaub, 2025)

## Slide 5
PINN Training Results
Model | RMSE (mGal) | MAE (mGal) | Rel. Error | USC δg Pred. | USC Error
Test 2 (tile norm.) | 0.5300 | 0.2821 | 0.31% | −95.39 mGal | 16.27 mGal
Test 1 (local norm.) | 0.2434 | 0.1383 | 0.20% ✓ | −79.30 mGal | 0.19 mGal
PINN-GM-III (benchmark) | — | — | 0.30% | — | —
Key Finding: Normalization scope is critical — local USC subgrid scaler (Test 1) achieves 16× lower prediction error than tile-wide normalization (Test 2). Relative error 0.20% beats the PINN-GM-III benchmark of 0.30%.
Test 1 Scatter (RMSE = 0.2434 mGal)
Predicted vs True δg tightly clusters along the perfect-prediction line. Residual histogram is sharply peaked at 0 with tail < ±2 mGal. USC origin prediction error: 0.19 mGal — confirms EKF Jacobian validity.
Free-Air Altitude Correction (Altitude Model)
GGMplus provides surface-level data only — all altitudes read the same δg at a given (lat, lon). To address this:
Δg_corrected = Δg_GGMplus − 0.3086 × alt
This free-air correction (0.3086 mGal/m) restores altitude-dependent variation in training data.

## Slide 6
EKF Navigation Results & Analysis
Chart: Position RMSE Comparison
| Raw IMU Dead Reckoning | PINN + EKF (Test 1) | PINN + EKF (Altitude Corrected)
RMSE (m) | 2957 | 53181 | 26547
ROOT CAUSE ANALYSIS
📶 Signal Too Weak
δg varies only 0.047 mGal over the 1.5 km path. Gravimeter noise = 0.5 mGal → SNR = 0.09.
🔍 System Unobservable
Hₓ = 2.5×10⁻⁵, H_z = 4.1×10⁻⁵ mGal/m → Kalman gain K ≈ 0 in East & Up axes. EKF update is ineffective.
✅ PINN: Working Correctly
0.20% prediction error + valid Jacobians confirmed. Architecture is sound — limitation is the test region's flat gravity field.
Conclusions & Future Work
Altitude correction halved EKF RMSE (53,181 m → 26,547 m), confirming altitude-dependent variation improves observability. Future work: (1) Redesign trajectory over high-gradient terrain (2) Navigation-grade gravimeter (~0.01 mGal, SNR > 1) (3) Use gradiometer (full 3D gradient) (4) Fuse with other non-GNSS sensors for full observability.